960H UTP Auto Gain Long Range Twisted Pair Transmission

Item No:  TTA111VEA-960H

TTP111VE Passive Video Transmitter + TTA111VHA-960H Digital Auto Gain Active Receiver

Features:

           To send 960H camera video signal over twisted pair cable.

- Eliminate the coaxial coax.

           Package include:  TTP111VE Passive Video Transmitter + TTA111VHA Digital Auto Gain

Active Receiver with power adapter.

          TTP111VE is passive type, no power required.

- TTP111VE compact size for easy installation at camera side.

- TTA111VHA-960H design for 960H video auto gain receiver built in two mode auto gain control.

- TTA111VHA-960H auto gain receiver built in transient protection and grounding lifting.

Installation View:

Panel View：

TTP111VE    									 TTA111VHA-960H

LED Indication：

Green:  Power  On/off

Auto Gain 2 Mode Function:

| MODE | Function |
| --- | --- |
| MODE1 | Fix the auto gain value after Automatic Equalization successful completed |
| MODE2 | Continuously and Automatically Equalization |

MODE1: Suitable for general application, If need the re- equalization, please switch to mode 2, then switch back to mode 1.

MODE2: Suitable for special environment application.  It automatically detects the cable length and continued to do equalization.

Troubleshooting:

The unit built in transient protection, please make sure to make grounding.

Specification：

| IT Em ITEM NO. | TTP111VE |
| --- | --- |
| Video Input (BNC Connector) | 1 |
| Video Input | 1V p-p, 75 Ohms |
| Cable | Twisted Pair CAT 5 |
| RJ-45 Output | Terminal |
| Power | X |
| Temperature | Operation: 0 to 55℃, Storage: -20 TO 85℃, Humidity: up to 95% |
| Dimension mm | 14.5 × 49.5 × 15.5 |
| Weight g | 18 |

| ITEM NO. | TTA111VHA-960h |
| --- | --- |
| Video Standard | NTSC / PAL |
| Video Input | Terminal Block / 100Ω / 1.4 Vp-p Max |
| Video Output | BNC / 75Ω / 1 Vp-p |
| Link Cable | CAT.5 (24 AWG) |
| Power Consumption | 100mA |
| Power Supply | DC 12V 500mA |
| Temperature | Operation: 0 to 55℃, Storage: -20 TO 85℃, Humidity: up to 95% |
| Dimension mm | 43.2 × 74 × 45.2 |
| Weight g | 50 |

# Text boxes

TTA111VHA-960H

960H Camera

1.2 KM (Max)

TTP111VE

960H DVR